HunterDouglas®  ProScreen External Roller Blind

| 1 | Brand | Hunter Douglas |
| --- | --- | --- |
| 2 | System | External Roller Blind ProScreen |

Fabric

| 3 | Fabric description | - HunterDouglas® Sergé - HunterDouglas® Carré |
| --- | --- | --- |
| 4 | Fabric colour | HunterDouglas® Sergé 108101 F/B 108108 Uni 108118 F/B 118118 Uni 108112 F/B 112101 F/B 116101 F/B 116116 Uni 117101 F/B 117117 Uni HunterDouglas® Carré 101208 101212 101216 101217 108301 108311 108317 108318 118118 118508 118517 F/B = Front or Back |
| 5 | Fabric properties | - Transparency / openness Sergé is 3% and Carré is 5% - Material Sergé and Carré is 42% Glass + 58% PVC - Fire resistance rating: M1 (French Norm NF P92-503) B1 (German Norm DIN 4102) C-S3,d0 (European Norm NEN-EN 13501-1) - Weather resistant - Reinforced on side with welded tape |

Dimensions

| 7 | Width (mm) | Limits are available via our nearest Hunter Douglas office. |
| --- | --- | --- |
| 8 | Height (mm) | Limits are available via our nearest Hunter Douglas office. |
| 9 | Quantity (pcs) | Numbers are available via our nearest Hunter Douglas office. |

Model

| 10 | Boxes | Self supporting head box, made of extruded aluminium, housing complete mechanism and fabric. - Sizes: 75x75 mm 85x85 mm 95x95 mm Without box profile with 95 mm endplates or with brackets - Box shape: Square (all boxes) Chamfered (75 and 85) - Profile finishing: RAL coated or natural anodized. - Endplates: made of zamak and coordinated with color aluminium profiles. Coated RAL 9022 when profiles are natural anodized. |
| --- | --- | --- |
| 11 | Side guiding | Two types of side guiding: Stainless steel cable, nylon coated. Aluminium. 5 side channels are offered equipped with black end plug. 27 x 20 mm for screw fixing in face 27 x 27,5 mm for click fixing 27 x 50 mm for side fixing 57 x 27,5 mm: double sided Recess 27 x 95 mm: Specific solution for blind installed in a niche – box 95 only. Profile finishing: RAL coated or natural anodized. |
| 12 | Rolling tube | Depending on blind sizes different tubes with throat to insert fabric are used: 47 mm in aluminium 63 mm in galvanized steel. |
| 13 | Bottom bar | There are 3 models of bottom bars: Aluminium 20 x 38 mm Aluminium 20 x 38 mm that reduces noise Aluminium 18 x 25 mm Steel Ø18 mm Finish aluminium bottom bar is natural anodized or RAL coated. Steel bottom bar is inserted in fabric pocket. |

Operation

| 14 | Operation type | The operation types are: - Side control with crank - Electric operation with motor and switch, remote or group control - Blind coupled to one of the previous models |
| --- | --- | --- |
| 15 | Operation side | - Crank right or left - Motor right or left - Coupled right or left |
| 16 | Operation crank | - Aluminium crank mechanism with 3,5:1 gear - The mechanism is equipped with a wind stop which limits the bottom position. - Deliverable in two colours: white grey - Standard available crank wand lengths are: 800, 1200, 1600, 2000, 2400 and 2800 mm. - Alternatively length according to customer specification - Standard fixed, alternatively detachable wand with funnel and wand clip |
| 17 | Operation motor | Available motor types: Quiet 230 V HD M 40 in tube 47 Quiet 230 V HD M 50 in tube 63 Other SOMFY (RTS) motors on request (mechanical, RTS, IO) according to screen size and customer specification |
| 18 | Motor controls | In accordance with customer specification |

Installation

| 19 | Installation box brackets | Box is supported by side channels conceiled stainless steel brachets when cable guiding is used. |
| --- | --- | --- |
| 20 | Installation specific brackets | Aluminium installation brackets for screens without a box. |
|  | Other installation brackets | Bottom fixation when cable guiding is selected. Aluminium square or seal bracket equipped with a spring. |
| 21 | Channel installation | Channel installation can be done in two ways: For a flat surface installation use plastic clips. For an installation on face or recess use screws. |
| 22 | Spacers | Spacers can be used to fix on face a blind equipped with single side channel. There are 3 lenghts of spacers: 7,5 mm 15 mm 30 mm Spacers have a black colour. |
| 23 | Recess | When a blind is installed in a niche, a Recess side channel is a good solution in combination with a box 95 mm or without a box with 95 mm brackets. |

Rolling

| 24 | Rolling direction | Back rolling in all combinations and front rolling only in combination with square head boxes. |
| --- | --- | --- |

Coupling

| 25 | Continuous box | Available with 75 and 85 mm boxes Maximum total width: 4500 mm Maximum blinds: 2 blinds Operation: crank or motor |
| --- | --- | --- |
| 26 | Separate boxes with a distance between boxes = 0 | Available with 75, 85 and 95 mm boxes Maximum sizes: Each blind cannot exceed maximum sizes of a single blind Maximum blinds: 3 blinds Operation: motor When channel guiding, single or double guiding can be used in the middle when the distance between boxes is zero. Maximum play for installation = 3 mm |
| 27 | Separate boxes with a distance between boxes > 0 | Distance between boxes is min. 33 mm and max. 150 mm Coupling connector is needed |