## PART 1:  CCA SYSTEM GENERAL

  - INTRODUCTION

Supply and fix Luxalon 30BD or 30BXD CCA System as manufactured by Hunter Douglas Architectural Products.

  - DESCRIPTION OF THE SYSTEM

The system will consist of box-shaped linear panels fixed to an adjustable suspension system which allows for individual panels to be removed by hand. System to feature open joins between the panels.

## PART 2: PRODUCT

_________m2 Luxalon® 30BD or 30BXD CCA Ceiling, featuring a 30 mm open joint and

consisting of:

  - PANELS

- 30BD, size 30x39 mm, rollformed from 0.5 mm Aluminium strip

- 30BXD, size 30x64 mm, rollformed from 0.5 mm Aluminium strip

Panels to be manufactured from prepainted stove enamelled aluminium, alloy, EN-AW-5050 or equivalent (according to EN 1396).

Panels have square sides and are plain/perforated, with/without non-woven acoustic textile. Panels to have a length of _________mm (manufacturer availability 800-6000 mm and on request > 6000 mm). Panels to be coupled in longitudinal direction by means of panel splices (30BD) or connected endcaps (30 BXD).

  - SUSPENSION

Rows of 0.95 Alu rollformed carriers shall be installed at ________centre on centre by means of adjustable suspensions at a distance of_______, centre on centre. Carriers will be joined by means of carrier splices. Carriers provided with prongs to hold panels in a module which is a multiple of 60 mm.

## PART 3: ADDITIONAL SPECIFICATIONS

3.1 PERIMETER PROFILES

- Wall L-profile 29.2x19.4 mm made of 0.5 mm thick aluminium

- Wall L-profile 45x18.5 mm made of 0.8 mm thick steel/aluminium

- Wall W-profile, 45x21x21`x18.5 mm, made of 0.8 mm steel/aluminium

3.2 PERFORATIONS

Manufacturer shall supply Luxalon® Multi-Panel panels with following perforation specifications:

- ( 1.0 mm, ( 2 mm with 23% open area: for 30BD

- ( 1.5 mm, ( 3 mm with 23% open area: for 30BXD

- ( 2.0 mm, ( 5 mm with 16% open area: for 30BD

Perforated panels to have a nominal plain border along the longitudinal panel direction to assure a maximum flatness and product stability:

- 30BD panels are perforated into the sides of the panels over a height of 18.5 mm for ( 1 mm and a height of 19.5 mm for ( 2 mm.

- 30BXD perforated into the side of the panel over a height of 41 mm.

  - ACOUSTICS

Manufacturer shall supply acoustic non-woven tissue, thickness 0.2 mm factory applied inside the panels. Alternatively the installer can place individually PE wrapped mineral wool pads.

  - COATING

Architect will make a colour selection from the standard Hunter Douglas colour range for Luxalon® CCA panels code no.____or a special colour will made to match.

The coating will consist of a tough and durable 2-layer polyester finish in nominal thickness of 20 microns, applied in a continuous coil-coating process ensuring uniform coating and absolute adhesion.

  - INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.