## PART 1: Solid Wood Grill System

  - INTRODUCTION

Supply and fix Hunter Douglas Solid Wood Grill System as manufactured by Hunter Douglas Architectural Projects.

  - DESCRIPTION OF THE SYSTEM

The system will consist of rectangular-shaped panels composed from square edged slats joined by rigid or flexible dowels, fixed by special clips to an adjustable suspension system.

## PART 2: PRODUCT

_________m2 Hunter Douglas Solid Wood Grill Ceiling consisting of:

  - PANELS

Luxalon Solid Wood Ceiling System, grill system slats, square edged, wood specie [  ]. Panels shall be constructed so that there are N number of slats per panel, The gap between the slats is G mm, the slats are W mm wide and are D mm deep. Slats shall be formed into panels 3300mm (max) x 500(max)mm. Panels shall be installed to leave a 15mm gap between the ends of the panels. Panels shall be separated along the ends of the panel utilizing wooden “T” profile.

  - SUSPENSION

The system’s suspension shall comprise of Hunter Douglas sendzimir galvanized black painted steel T bar at 1200mm centre-to-centre. The T bar shall be suspended at 1200mm centres using adjustable hangers. Panel cantilever shall not exceed 100mm, steel T bar cantilever shall not exceed 100mm. Each panel shall be suspended to each T bar with (depending on size and weight of the grill) at least four dowel rail suspension clips attached in alternating direction.

## PART 3: ADDITIONAL SPECIFICATIONS

3.1 PERIMETER PROFILES

Perimeter Trims shall not be used. The panels shall be installed as to leave a 15mm gap at the ends and sides of the panels.

3.2COATING

Slats will be finished on 4 sides with a clear UV resistant varnish. Optionally slats can be stained on 3 or 4 sides in a colour to be agreed upon.

  - IMPREGNATION

Panels can optionally be fire-retardant impregnated to reach a minimum classification of [  ].

  - INSTALLATION

All materials shall be installed in strict compliance with all local codes, ordinances and manufacturers recommendations including specific additional requirements as may be called for in the specifications or shown on the drawings.

Services fittings: Site formed apertures shall be formed within the ceiling panels to suit appropriate luminaries/sprinkler heads/smoke detectors and light fittings. Stiffeners shall be used where necessary to support accessories